## Centrifuge model test on pile group effect of pile foundation reinforced by micropile

## Masashi ITANI1

###### Toshinobu KAWAMURA1

###### Seiichi ONODERA1

###### Takeshi OSHITA1

###### 1Public Works Research Institute, Independent Administrative Institution, Japan

## ABSTRACT

After the occurrence of Hyogo-ken Nanbu Earthquake in 1995, it became an important theme that the existing structure was reinforced for earthquake resistance in Japan.   In the most bridges, the piers are reinforced by winding steel plate.   On the other hand, the reinforcement of the foundations under the footing is rarely conducted because of the limited working clearance and the large amount of cost for the conventional reinforcing methods.   However, in order to improve the earthquake resistance of the whole bridge, it is necessary to reinforce the bridge foundation as well.   Therefore, the research and development is being carried out to realize the new reinforcing method for the bridge foundation using the Micropile (hereinafter referred to as “MP”).   By the new method with the MP, the reinforcing work is possible even in the limited clearance under the bridge girders and the cost is also cheaper than that of conventional.   However, at the design stage, the effect of pile group in the pile foundation reinforced by the MP has not been clarified.   Then, we conducted the horizontal loading test for the pile foundation model reinforced by MP in the centrifugal field in order to clarify pile group effect.

Keywords: Micropile, Earthquake strengthening, Pile group effect, Load sharing

## 1. INTRODUCTION

By the earthquake (magnitudes of 7.2 on the Richter scale) which occurred in the southern part of Hyogo Prefecture in Japan in 1995, many bridges and viaducts have been largely damaged such as collapse of the bridge pier and falling of the bridge girder, which had undergone the seismic design of the then design standard.   Therefore, seismic design standard for highway bridges and viaducts was amended in 1996 considering the damage by the said earthquake.  According to this amended design standard, intensive retrofitting work for the bridge piers and girders has being conducted nationwide. In order to improve the earthquake resistance of the whole bridge, the following bridge foundations are also needed to be reinforced.

- The foundation whose design has not met the new design standard yet, though has undergone the old design standards.

- The foundation in which the effect of the liquefaction is not considered.

In case of the reinforcement of bridge foundations such as  and , the additional pile method is mostly used as the conventional method.  However, this conventional method needs wide working space, high working clearance, an amount of cost and long construction period for adding piles around the footing and widening the footing, and at many sites, this conventional method is not able to be carried out due to the said restrictions.   Therefore, the development of the rational and efficient earthquake strengthening method with low construction cost is necessary and, we aim at establishment of the earthquake-resistant reinforcing method for the existing foundation using the MP instead of additional pile for clearing the problems which arise in the conventional methods.

## 2. TEST PROPOSE

It places large number of MPs around the existing piles, when the pile foundation of the existing bridge is reinforced by the MP, and it will be combined with the footing.   In the case that the horizontal force acts on such existing foundation and that the piles are greatly deformed each pile affects it to each other, the subgrade reaction which acts on each pile is generally different by positions and intervals of the pile, etc.   What is called pile group effect occurs.   Most experiments on the pile group effect up to now are by the pile of "same material" or "equal diameter".     However, it becomes composite pile foundation of "existing pile with the large diameter" and "MP with the small diameter", when the existing foundation is reinforced by the MP.   It has not yet clarified the behavior of each pile and pile group effect in such case.   Then, we carried out the horizontal loading test of model foundation composed of two kinds of pile with different diameter, large diameter piles as existing pile and small diameter piles as MP, in centrifugal field (20G) in order to clarify pile group effect of the pile foundation reinforced by the MP.

## 3. TEST OUTLINE

| Pile type | Material | Diameter | Thickness | Length | EI |
| --- | --- | --- | --- | --- | --- |
|  |  | (mm) | (mm) | (m) | (kN・m2) |
| Existing Pile | Model | Steel | 30 | 1 | 0.5 | 1.927E+00 |
|  | Full scale | Steel | 600 | 20 | 10 | 2.084E+05 |
| MP | Model | Steel | 9 | 0.5 | 0.5 | 2.430E-02 |
|  | Full scale | Steel | 180 | 10 | 10 | 3.891E+03 |

In the experiment, we used centrifugal test equipment which Public Works Research Institute (PWRI) possesses.  A 1/20 scale model of a pile was used.   The model of the existing pile was assumed as the steel pipe pile and the model of the reinforcing pile was assumed as the MP.  The dimensions of the pile model are shown in Table 1 and comply with similarity rule with full scale.  And, the model pile is made of stainless steel and is hollow pipe.  In the model pile, two strain gauges were fixed in diagonal directions at each point in order to measure flexural strain, as shown in Fig. 1.   The head of each pile was combined with the footing, and the tip of the pile was fixed to the bottom plate of the earth tank. Compaction was performed by charging dry sand and compacting by vibrator every 5 cm to make the model ground after setting the test piles. As a result, homogeneous ground of about relative density Dr = 85% (γt = 16.8 kN/m3, φ = 42.5°, c = 0kN/㎡) was made. The experiments were conducted under centrifugal acceleration of 20 G.   The loading horizontally pushed the side of the footing in one direction by mechanical jack at constant speed of 1.0 mm/min.   Then, the load - displacement relation of footing and strain of the pile at each point were measured.

## 4. TEST CASES

The 11 arrangement patterns of piles shown in Fig. 2 were tested.   Tests of Case 3 and 4 were conducted twice with different ground conditions, and condition　　　 of model ground of Case 3-2, 4-2, 10, and 11 were a little different from that of other case.   A single existing pile and MP were used in Case 1 and 2, respectively.   Case 4 was reinforced pattern of Case 3 by MP.     Case 5 had more MP than Case 4.   Case 6 and 7 were rotated pattern of Case 4 and 5, respectively. In Case 8 and 9, the interval between existing piles and MP was doubled for Case 4 and 5, respectively.   Case 10 and 11 were the patterns in which MPs were set at an oblique angle for Case 4.

## 5. TEST RESULTS

The following experimental results were expressed in converted full scale.   The horizontal displacement of footing has been standardized at the pile diameter of the existing pile.   The horizontal displacement in the Case of single MP, Case 2, also standardized at the pile diameter of the existing pile.

5.1　Load - displacement relation

The load - displacement relations for all patterns are shown in Fig. 3 to 6.   The pile group efficiency for Case 3 to 9 and formulae for computation are shown in Table 2.   The case in which the existing pile is reinforced in front and in the rear by MP is shown in Fig. 3.   The resisting force against the horizontal load increases in Case 4 and 5 by setting the MP, thus confirming the reinforcement effect of MP.

Case 5 has more MP than Case 4-1. In Case 5, the resisting force against horizontal load increases proportionally to the number of MP.   This proves that the pile group effect among MPs in the same row is small, if the interval of each MP in front and in the rear of the existing piles is 500 mm (in full scale) which is equivalent to 2.7 times the diameter of the MP (180mm in full scale) .

The effect of the number of MP is shown in Fig. 4, when the both sides of the existing pile are reinforced by MP (Case 6 and 7).   As well as the case in which MP was placed in front and in the rear of the existing pile, the number of MP affected the horizontal load. However, the increasing rate of load is smaller than that in cases in which MP was placed in front and in the rear of the existing pile.   In comparison with Case 4-1 and 5, Case 6 and 7, in which the side of the existing pile is reinforced by MP, has higher resisting force than Case 4-1.   However, there is little difference in load strength between Case 5 and 7 in which the existing pile is reinforced with more MP.    Fig. 5 compares the effect of the interval between MP and existing pile, when MP was placed in front and in the rear of the existing pile. In Case 4-1 and 5, the interval between MP and existing pile is about 1.7 times that of the existing pile diameter, and in Case 8 and 9 the interval is about 3.3 times.   The effect on the horizontal load of increasing the interval between MP and existing pile is small, and there is little difference in the load-displacement curve.   Next, the effect of obliqueness of MP is shown in Fig. 6, proving that the resisting force against horizontal load increased with increasing angle of inclination.

  - Sharing of shear force at the pile head (comparison by configuration interval and arrangement of MP)

Fig. 7 shows the sharing of the shear force at the head of each pile at the yield point in Case 3 to 9.   It compares Case 6 and 7 in which MP is placed on the side of the existing pile, with Case 4-1 and 5 in which MP is placed in front and in the rear of the existing pile.   In Case 4-1 the MP in the rear row carries about half the load compared with the MP in the front row, and the reinforcing effect of rear MP is not enough. In Case 6, the horizontal load of the front and rear MP was almost the same.   Each MP shares equal load when fewer MPs were placed on the side of the existing pile.   For this reason, Case 6 in which MP is placed on the side of the existing pile is larger than Case 4-1 in which MP is placed in front and in the rear of the existing pile, regarding the resisting force against horizontal load.   However, Case 7 which had more MP than Case 6 had slightly lower sharing rate on the rear MP than that on the front MP.   Therefore, the increasing rate of horizontal load between Case 6 and 7 was less in comparison with Case 4 and 5.   Thus, pile group effect occurs among MPs in the line, when more MPs were placed on the side of the existing pile with interval between each MP of about 2.7 times the diameter of MP.   The load sharing rate of each pile in Case 8 and 9 in which the interval between MP and existing pile was larger was almost equal to Case 4-1 and 5 with smaller interval.   And, the MPs in the rear row did not sufficiently resisting effect, because the pile group effect between the front and rear piles was not improved even if the interval between MP and existing pile was multiplied up to about 3.3 times the diameter of the existing pile.   Therefore, the effect of the front piles to the rear piles must be considered.

5.3　Effect of oblique piles

Fig. 8 shows the sharing of shear force at the pile head in Case 10, and 11 in which MPs were installed obliquely.    The load sharing rate of MP in the front row increases from 8% to 30% as the inclination angle of MP increases, and the load sharing rate of the existing piles in the front row falls from 50% to about 35%.   There is little change of the load sharing rate on existing piles and MP in the rear row.   Thus, the load carried by MP in the front row increases when MP is oblique.   Fig. 9 shows the axial force of each pile at the pile head in Case 4-2, 10, and 11.   The axial force on MP in the front row increases with the increase of inclination angle.   In comparison, the axial force on MP in the rear row does not change very much.   These results show that the force acting on MP in the front row increases when MP is oblique.   As a result, the force which restrains the deformation of the foundation increases.

5.4　Distribution of bending moment

The bending moment was calculated from flexural strain.   The bending moment distribution of Case 4-1, 6, and 8 is shown in Fig. 10.   In Case 4-1 and 8 in which the MP was placed in front and in the rear of the existing pile, the depth of the largest bending moment of the MP in the front row was not deeper than that of the MP in the rear row.   Also, the value of the largest bending moment on the MP in the front row tended to be larger.   However, there was little difference of the depth and value of the largest bending moment between the front MP and rear in Case 6 in which the MP was placed on the side of the existing pile.   This is because the front and rear MPs bore the equivalent horizontal load.

5.5　　Reduction of subgrade reaction according to arrangement of piles

By the differentiation in twice of the approximation of the bending moment in spline curve and dividing it by the pile diameter, subgrade reaction was calculated.   The distribution of horizontal subgrade reaction in Case 4-1 and 6 is shown in Fig. 11.   The subgrade reaction increases with the increase in horizontal load.   However, the subgrade reaction tends not to increase near ground surface, when it reaches a certain value.   This condition is called the ultimate subgrade reaction.   The straight broken line shown in the Fig. 11 shows passive earth pressure and the dotted line shows ultimate subgrade reaction.   Table 3 shows the ratio of coefficient of ultimate subgrade reaction which is standardized by the front MP for Case 4-1 and 6.   In Case 4-1 in which MP was placed in front and in the rear of the existing pile, the ratio of the existing pile in the front row is small.   This result shows the pile group effect by MP in front of the existing pile.   In Case 6 in which MP was placed on the side of the existing pile, the ratio of existing pile in the front row and front MP is the same.     This is because the pile group effect does not occur by front MP.

6. CONCLUSIONS

The following results were obtained.

1)  MP effectively reinforced the existing pile foundation.

2)  The pile group effect does not occur among MPs in the same row, when MP was placed in front and in the rear of the existing pile with the interval of about 2.7 times the diameter of MP.

3)  The rear MPs are affected by the pile group effect, when MP was placed on the side of the existing pile with the interval of about 2.7 times the diameter of MP.

4)  Even if the interval between the existing pile and MP is 3.3 times of the diameter of the existing pile, the pile group effect occurs.

5)  When MP was set obliquely, the MPs in the front row take much effect, and the reinforcing effect increased.

6)  Pile group effect occurred to some extent when MP was placed in front of the existing pile.

This experiment was conducted in only model sand ground.   It is necessary to also examine the pile group effect in clayey ground, and to examine the ratio of the upper limit of subgrade reaction of existing piles in the front row.

REFERENCES

1) Japan Road Association: Specification for Highway Bridges Part IV Substructure, 1996 (in Japanese)

2) Y. Ichimura et al.: The Centrifugal Model Tests on Load Sharing between Existing Pile and Micropile: International Workshop on Micropiles, 2000.

# Text boxes

Fig.9  Axial Force

Fig. 7 Horizontal Load Sharing Rate

Case 4―1

Table 2 Pile group efficiency

|  | Pile group efficiency (%) |
| --- | --- |
| Case 3 | 79.5 |
| Case 4 | 64.9 |
| Case 5 | 67.5 |
| Case 6 | 77.6 |
| Case 7 | 73.2 |
| Case 8 | 66.5 |
| Case 9 | 68.3 |

Table 1 Test pile specifications

Fig. 1 Test Setup

Fig. 2  Loading test cases

Fig. 8 Load Sharing Rate in Reinforcing by Oblique Piles

Fig. 11 Subgrade Reaction Distribution ( Case 4-1 and 6 )

Fig.10 Bending Moment

Fig. 3 Load-displacement relation

（for varying number of MP）

Fig. 4 Load-displacement relation

( for varying number of MP on the side of the existing pile )

Fig. 5 Load-displacement relation

（for varying intervals between MP and existing pile）

Fig. 6 Load-displacement relation

（for varying inclination angle of MP ）

Case 4-1

Case 4-1

Case 8

Case 8