Pile/Footing Connection

Coordinator: T. Yamane (Japan)

Current state of regional practice for the design of the pile/footing connection

Japan: plate on casing, sometimes with stiffeners, always shop-fabricated (HMP)

North America: seldom based on development length. Most often plate on casing or plate on bar via nut (dependent on load). Connection design often the realm of non-micropile specialist/structural engineer ( all regions. Also dependent on situation (i.e. new pile cap vs. existing foundation being retrofitted)

Europe: Mostly via bearing plate – field welding not allowed; shop welding difficult to coordinate & construct. Official approvals exist ( more desirable for contractors to adopt a common detail.

Available publications detailing design procedures

Japan: Specifications for Highway Bridges

North America: ACI, AASHTO, IBC (FHWA)

Europe: DIN 1045 ( EN 1992 (EC2), EN 1993 (EC3), BS 8 -110

Seismic considerations

Japan : as per specifications for Highway Bridges

North America: battered piles not adopted by transportation due to risk of rupture during loading event

Europe: (None?) EN 1998

Applicable building codes (see above)

Construction considerations

Japan: avoid air pocket below plate!

In the case of existing footings, a real problem exists in the potential difference between assumed or expected foundation design & actual construction

Lack of existing reinforced concrete foundations in Europe

Quality assurance/quality control considerations

2% to 5% or 100% of piles tested

0% of connections tested (sometimes pre-construction, full-scale tests)

Effective Stress Analysis of Micropile Bond Stresses

Coordinator: R. Frank (France)

- Theoretical vs. Empirical

  - “Impossible to predict qs theoretically”

  - B σ vo’ – “all our ignorance” (with respect to B)

  - we all use empirical methods

  - qs = f (soil (ID, IC, etc.), installation/drilling/injection method, etc.) ( all of this comes from full-scale field test data

  - Full-scale field tests for the specific project: trend for standards piles is even more pronounced for HMP

  - Influence of pile length (load transfer pb)

  - Influence of qs with length at least for l < 15 meters; influence of depth as such is still debated

- Impossibility to describe history of stresses and nature of bond

- Research with hopes only for load transfer pb

- Some data is available but not clearly recognized and linked to empirical methods

Compilation of Pile Test Data

Coordinator: M. Turner (United Kingdom)

IWM – “Put some in, Take some out”

Do we want a database? If so, how do we get it? How will you (each of us) help?

  - Need to capture load test data. It’s out there.

  - Challenge to obtaining data

  - MICROFOR – United States

  - The data is a “mine” of information

  - Strategic goal is to provide “data” for calibration

  - Analysis also – not just a list

  - How big is the mine?

  - Mike Turner: 20 in soils, 15 – 20 in rock, 20 – 30 in DLT rock, 20 ???, anchor tests around 40?

  - Donald Bruce: 40 tests in U.S. per year x 15 years = 600 tests (40-60)

  - Japan: (no reply given)

  - Europe: (no reply given)

| Data | Contractor | Consultant | Client | Gov’t | Trade Associations (i.e. JAMP) | Key persons |
| --- | --- | --- | --- | --- | --- | --- |
| Country |  |  |  |  |  |  |
| North America | ( |  |  |  |  |  |
| United Kingdom | ( | ( |  |  |  |  |
| Japan | ( |  |  | ( |  |  |
| Europe |  |  |  |  |  |  |

Challenges

Why don’t we have the data already?

- Lack of clear purpose

- No one asked

- Reluctance of contractors (some) to divulge

- Unable to transfer applicability

- No funding for processing

- No champion for the battle

- Bad previous experience

Strategy

- Find a champion (person). IWM to define purpose. Five individuals?

- Business Plan to IWM? (Donald Bruce)

- Reciprocity

Knowledge/awareness of IWM

- North America: Positive

- Europe: low (except northern Europe)

- Japan: positive